## Slide 1: Seismic to Well Ties
Objectives of the seismic - well tie
What is a good well-seismic tie?
Comparing well with seismic data
Preparing well data
Preparing seismic data
How to tie synthetics to seismic data.
Pitfalls
Schroeder (2006) Courtesy of ExxonMobil

## Slide 2: Objectives of Well-Seismic Ties
Well-seismic ties allow well data, measured in units of depth, to be compared to seismic data, measured in units of time.
This allows us to relate horizon tops identified in a well with specific reflections on the seismic section.
A “synthetic” is a 1D, zero offset seismic model using sonic and density logs, a wavelet and a time to depth function.
The synthetic trace is compared to the real seismic data collected near the well location
Schroeder (2006) Courtesy of ExxonMobil

## Slide 3: North Sea Rock Property Data

## Slide 4: North Sea Well Tie
GR SW PHI VP RHOB P Imp Synth

## Slide 5: Measurements In Time and In Depth
Schroeder (2006) Courtesy of ExxonMobil
Surface Elevation
Base of Weathering
Seismic: Time Units
Log: Depth Units
Kelly Bushing
Elevation (KB)
True Vertical depth (TVD)
Measured Depth (MD)
Two-way time (TWT)
SHOT
RECV
Measured Depth (MD)
Depth Below Mud Line
Sea Floor

## Slide 6: Comparison of Seismic and Well Data
Seismic Data
Samples area and volume
Low frequency 5 - 60 Hz
Vertical resolution 15 - 100 m
Horizontal resolution 150 - 1000 m
Measures seismic amplitude, phase, continuity, horizontal & vertical velocities
Time measurement
Well Data
Samples point along well bore
High frequency, 10,000 - 20,000 Hz
Vertical resolution 2 cm - 2 m
Horizontal resolution 0.5 cm - 6 m
Measures velocity, density, resistivity, radioactivity, SP, …
Depth measurement
Schroeder (2006) Courtesy of ExxonMobil
100 m
100 m

## Slide 7: Seismic-Well Tie Flow-Chart
Schroeder (2006) Courtesy of ExxonMobil
Seismic Data
Estimate
Wavelet
Data Processing
Seismic Modeling
Well -
Well – Seismic Tie
Well Data
Data Processing
Check Shots/ Time Depth
Synthetic Seismic Trace
Real Seismic Trace

## Slide 8: Check Shot/VSP Data
Schroeder (2006) Courtesy of ExxonMobil
Seismic Shot
Borehole Geophone
Time
Depth
Check shots measure the vertical one-way time (OWT) from surface to various depths (geophone positions) within the well
  Used to calibrate the relationship between well depths and times calculated from a sonic log

## Slide 9: Wavelets
Minimum Phase
RC
Positive
Reflection
Coefficient
Impedance
Zero Phase
Quadrature
Phase
Common Wavelet Shapes
Two options for defining a wavelet:
Use software that estimates the Wavelet based on a ‘window’ of the real seismic data at the well (recommended)
  Statistical (seismic only) > Best initially
  Deterministic (seismic & well) > Best after good initial well tie
Use a standard Wavelet shape specifying polarity, peak frequency, and phase:
  Minimum phase
  Zero phase
  Quadrature
Schroeder (2006) Courtesy of ExxonMobil

## Slide 10: Using the Water Bottom

## Slide 11: The Modeling Process
We use the velocity (sonic) and density logs to compute an impedance log
We calculate the reflection coefficients from impedance: DI/(I1+I2)
We convolve the wavelet with the RC series to get individual wavelets
Each RC generates a wavelet whose amplitude is proportional to the RC
We sum the individual wavelets to get the synthetic seismic trace
Schroeder (2006) Courtesy of ExxonMobil
Velocity
Density
Impedance
=
x
Lithology
Reflection
Coefficients

*

Wavelet

Synthetic
Shale
Sand
Shale
Sand
Shale

## Slide 12: Tying Synthetic to Seismic Data
Position of
Synthetic Trace
Time (ms)
Schroeder (2006) Courtesy of ExxonMobil
Position synthetic trace on seismic line.
  Project synthetic along structural or stratigraphic strike if well is off line (2D)

## Slide 13: Tying Synthetic to Seismic Data
Time (ms)
Schroeder (2006) Courtesy of ExxonMobil
Synthetic Trace
Position synthetic trace on seismic line.
  Project synthetic along structural or stratigraphic strike if well is off line (2D)
Reference datum of synthetic to seismic data (usually ground level, sea level or seismic datum)
  Without check shots, estimate start time of first bed or tie to known horizon

## Slide 14: Tying Synthetic to Seismic Data
Synthetic Trace
Time (ms)
Schroeder (2006) Courtesy of ExxonMobil
Position synthetic trace on seismic line.
  Project synthetic along structural or stratigraphic strike if well is off line (2D)
Reference datum of synthetic to seismic data (usually ground level, sea level or seismic datum)
  Without check shots, estimate start time of first bed or tie to known horizon
Shift synthetic in time to get the best character tie (if needed)
  Not unusual, but need to investigate why you need a shift

## Slide 15: Tying Synthetic to Seismic Data
Schroeder (2006) Courtesy of ExxonMobil
Accept the tie that yields best character tie with least time shift in the zone of interest (reservoir)
Reservoir
Zone
Seal
The top of the reservoir should be mapped on this peak (red)

## Slide 16: Assumptions for Synthetic Well Ties
Schroeder (2006) Courtesy of ExxonMobil
Seismic Data
  Noise free
  No multiples
  Relative amplitudes are preserved
  Zero-offset section
Synthetic Seismograms
  Logs representative of the earth sampled by the seismic data
  Normal incidence reflection coefficients
  Multiples ignored
  No transmission losses or absorption
  Isotropic medium (vertical and horizontal velocities are equal)

## Slide 17: Common Pitfalls
Schroeder (2006) Courtesy of ExxonMobil
Error in well or seismic location
    washout zones, drilling-fluid invasion effects
Log data quality
  washout zones, drilling-fluid invasion effects
Seismic data quality
  noise, multiples, amplitude gain, migration, etc
Incorrect wavelet
  Polarity, frequency, and phase (Try a different wavelet; use extracted wavelet)
Incorrect 1-D model
  Logs, check shots need further editing
  Incorrect start time or improper datuming
  Amplitude-Versus-Offset (AVO) effects
  Bed tuning …

## Slide 18: Pitfalls – AVO
Offset
Time
Multiples
    R() ~= R0COS2 + 2.25SIN2
=2-1,  (Poisson's Ratio)
 = Angle of incidence
CDP Location
Shallow Beds
Deep Beds
Offset
Sources
Receivers
Depth
Time

Notes: On this slide I have an example of AVO information in a gather.
On the right is the CDP acquisition diagram. You can see that as the offsets vary, the angle that the energy reflects off the beds changes. As we saw in the last slide, this changes the contrbutions that Impedance and VP/Vs make to the reflection amplitude.Thus, at every different offset, the reflectivity will be different.
On the gather we can see some obvious example of this.
High amplitude on near - Class I. Increases with offset indicating that it’s a valid hydrocarbon anomaly.
Deeper reflection - moderate to low amplitude on near. Class II which might have been missed on stacked data. Here we can see that it has a dramatic increase in amplitude with offset - Hydrocarbons.
If you look more closely you canb see that eacj reflection has a unique change in amplitude with offset. Many that would be similar oin stacked data are very different in the gather.
Two shallower moderate amplitude reflection. On the stacked data they are brighter than the class 2 anomaly. However on the gather they decrease in amplitude with offset, indicating no hydrocarbons.

## Slide 19
Hampson Russell Exercise

## Slide 20
Hampson Russell Exercise

## Slide 21
Hampson Russell Exercise – Check Shot Correction

## Slide 22
Hampson Russell Exercise – Check Shot Correction

## Slide 23
Hampson Russell Exercise – Check Shot Correction

## Slide 24
Wavelet – 30Hz Ricker Quad
Hampson Russell Exercise – Ricker Wavelet

## Slide 25
Hampson Russell Exercise – Time Shift

## Slide 26
Hampson Russell Exercise – Ricker Wavelet

## Slide 27
Wavelet – Statistical vs. 30Hz Ricker Quad
Hampson Russell Exercise – Statistical Wavelet

## Slide 28
Hampson Russell Exercise – Statistical Wavelet

## Slide 29
Wavelet – Statistical vs. Using Wells
Hampson Russell Exercise – Wavelet Using Wells

## Slide 30
Hampson Russell Exercise – Wavelet Using Wells

## Slide 31
Hampson Russell Exercise – Well Tops Report

## Slide 32
Hampson Russell Exercise – Well Tops Report