## Slide 1: Seismic Resolution
Vertical Resolution
  Resolution vs. Detection
  Thin Bed Response and Tuning
Lateral Resolution
  Fresnel Zone
  Migration and Lateral Resolution
Scenario Modeling
Gassmann Fluid Substitution

## Slide 2: Detection vs. Resolution - Analogy
You are driving at night.
You spot a light in the distance.
Is it a car or a motorcycle???
Aha, it is a car!
Schroeder (2004) Courtesy of ExxonMobil

## Slide 3: Resolution vs. Detection
Detection: Ability to identify that some feature exists
Resolution: Ability to distinguish two features from one another
Detection limit is always smaller than the resolution limit
Detection limit depends upon Signal-to-Noise, impedance contrast
Schroeder (2004) Courtesy of ExxonMobil

## Slide 4: Vertical Resolution
What is the minimum vertical distance between two subsurface features such that we can tell them apart seismically?
Shale
Sand
Sd
Shale
Baseline
Gamma Ray
For Example:
Based on seismic data, could you determine that there is a thin shale layer between the two sands?
Schroeder (2004) Courtesy of ExxonMobil

## Slide 5: Thick Bed Response
Schroeder (2004) Courtesy of ExxonMobil
A thick bed is one that has a thickness > ld/2
Impedance
Composite
Wavelet 1
R. C.
Wavelet 2
NO
Interference
Top of Bed
Response
Base of Bed
Response
lt
B
A
C
ld = lt*Vint

## Slide 6: Partial Interference
Schroeder (2004) Courtesy of ExxonMobil
Some
Interference
2nd half-cycle from Wavelet 1
and 1st half-cycle from Wavelet 2
form a trough doublet
Some
Interference
B
A
C
lt
Top of Bed
Response
Base of Bed
Response
Thickness ~ 0.45* ld
Impedance
Composite
Wavelet 1
R. C.
Wavelet 2

## Slide 7: Maximum Constructive Interference - Tuning
Schroeder (2004) Courtesy of ExxonMobil
Thickness ~ ld /4 to ld /6
B
A
C
Impedance
Composite
Wavelet 1
R. C.
Wavelet 2
2nd half-cycle from Wavelet 1 and 1st half-cycle from Wavelet 2 are completely in phase
resulting in 2x amplitude
lt
Maximum
Interference
Top of Bed
Response
Base of Bed
Response

## Slide 8: Destructive Interference – Below Tuning
Schroeder (2004) Courtesy of ExxonMobil
Thickness = ld /16
B
A
C
Impedance
Composite
Wavelet 1
R. C.
Wavelet 2
Wavelets destructively interfere. Arrival times don’t change but amplitude does
lt
Destructive
Interference
Top of Bed
Response
Base of Bed
Response

## Slide 9: Determining Vertical Resolution
Schroeder (2004) Courtesy of ExxonMobil
Period
(ms)
wavelength =
period X velocity
Pulse
Input Parameters:
Velocity at the zone of interest
Peak Frequency of the wavelet at the zone of interest
Computations:
Period ~ 1/Peak Frequency
Wavelength ld = Period * Velocity
Limit of Vertical Resolution ~ Wavelength ld /4

## Slide 10: Typical Vertical Resolution
Shallow Event
  Velocity = 2000 m/s
  Wavelet: Center Frequency = 50 Hz
    Period = 1 / 50 = .020 sec = 20 ms
    Wavelength = .020 x 2000 = 40 m
  Limit of resolution ~ 40 /4 = 10 m
Deep Event
  Velocity = 3000 m/s
  Wavelet: Center Frequency = 20 Hz
    Period = 1 / 20 = .050 sec = 50 ms
    Wavelength = .050 x 3000 = 150 m
  Limit of resolution = 150 / 4 = 37.5 m
Schroeder (2004) Courtesy of ExxonMobil
Frequency
Velocity
As depth increases:

## Slide 11: Summary: Vertical Resolution
Resolution is the ability to distinguish distinct events
Thin bed response occurs below tuning thickness
Short-duration seismic pulses are preferred
  Broad bandwidth, zero-phase pulses are best
  Pulses with minimal side-lobe energy enhance interpretability
To Improve Resolution
  Bandwidth can be increased by deconvolution
  Frequencies to be included must have adequate S/N
Schroeder (2004) Courtesy of ExxonMobil

## Slide 12: Seismic Resolution
Vertical Resolution
  Resolution vs. Detection
  Thin Bed Response and Tuning
Lateral Resolution
  Fresnel Zone
  Migration and Lateral Resolution
Scenario Modeling
Gassmann Fluid Substitution

## Slide 13: What Is Lateral Resolution?
Would we image the narrow horst?
Would we image all three channel sands?
Schroeder (2004) Courtesy of ExxonMobil

## Slide 14: Lateral Resolution
Neidell & Poggiaglioimi (1977)
What is the minimum horizontal distance between two subsurface features such that we can tell them apart seismically?

## Slide 15: The Fresnel Zone
An event observed at a detector is reflected from a zone of points
The raypaths from source to detector which differ in length by less than a quarter wavelength can interfere constructively
The portion of the reflector from which they add constructively is the Fresnel zone
Changes that occur within this zone are difficult to resolve
The size of the Fresnel zone depends upon the length and shape of the wavelet and the depth of the reflector
Schroeder (2004) Courtesy of ExxonMobil

## Slide 16: Migration Reduces Lateral Smearing
Schroeder (2004) Courtesy of ExxonMobil
800 m
Ideal / Model
Response
Image After
Migration
Stack
No Migration

## Slide 17: Good Migration Enhances Resolution
Schroeder (2004) Courtesy of ExxonMobil
Standard Migration
High-end Migration

## Slide 18: Fresnel Zone Equations
Schroeder (2004) Courtesy of ExxonMobil
where:
Fd = Fresnel Diameter
Vavg = Average Velocity
T = Time
F = Frequency of Pulse
λd = Wavelength
Post-Migration
Fd = λd /4 = Vavg /4 F
Pre-Migration
Fd = Vavg T/F

## Slide 19: Typical Lateral Resolution
Schroeder (2004) Courtesy of ExxonMobil
Shallow Event
  Time = 1.0 s
  Vint = Vavg = 2000 m/s
  Wavelet = 50 Hz
  PreMig Fresnel Diameter = 282 m
  PostMig Fresnel Diameter = 10 m
Deep Event
  Time = 5.0 s
  Vint = 4600 m/s
  Vavg = 3800 m/s
  Wavelet = 20 Hz
  PreMig Fresnel Diameter = 1900 m
  PostMig Fresnel Diameter = 47.5 m

## Slide 20: Fresnel Zone Circles
Schroeder (2004) Courtesy of ExxonMobil
Shallow Window
282 m pre-migration
10 m post-migration
1 km
Deep Window
1900 m pre-migration
47.5 m post-migration

## Slide 21: Summary: Lateral Resolution
Schroeder (2004) Courtesy of ExxonMobil
Migration enhances lateral resolution
Large aperture (receiver cable length) is needed for high lateral resolution
Fine spatial sampling is needed for high lateral resolution
Prestack migration provides better lateral resolution than post stack migration
Depth migration provides better resolution than time migration

## Slide 22: Seismic Resolution
Vertical Resolution
  Resolution vs. Detection
  Thin Bed Response and Tuning
Lateral Resolution
  Fresnel Zone
  Migration and Lateral Resolution
Scenario Modeling
Gassmann Fluid Substitution

## Slide 23: Scenario Modeling - Pitfalls
Low
impedance
sand
Low
impedance
shale
High
impedance
sand
Always be sure that the rocks you’re interested in tie to the attribute your measuring!

## Slide 24: Scenario Modeling - Thickness vs. Seismic Amplitude
Wedge Model
    (20 Hz Ricker - 10000 f/s)
    Period = 1 / 20 = .050 sec
    ld = .050 x 10000 = 500 ft
Amplitude of Top Reflection
360’
0’
~ ld /4
125’
Notes: What we care about is how different are the properties of hydrocarbons and water. The greater the difference, the greater the change in reflection amplitude.
EXPLAIN SLIDE

## Slide 25: Can I Predict Reservoir Presence?
Well B
Well C
Well E
Well A
Well D
Well F
Net Sand Predicted from Amplitude
Well B
71’
Well D
15’
Well
Net Sand
Well B
Well E
Well C
Well A
Well D
Well F
71
21
48
62
15
44
Pred.
68
29
42
53
14
36

## Slide 26: Seismic Resolution
Vertical Resolution
  Resolution vs. Detection
  Thin Bed Response and Tuning
Lateral Resolution
  Fresnel Zone
  Migration and Lateral Resolution
Scenario Modeling
Gassmann Fluid Substitution

## Slide 27: Fluid Substitution - Biot-Gassmann Equations
Russell (2015).
The existing rock

## Slide 28: Fluid Substitution - Biot-Gassmann Equations
Russell (2015).
Reservoir Conditions
Dry Framework
Fluid Substitution
K - Bulk Modulus
µ - Shear Modulus
r - Density
rdry = rsat - f * rfl(g,o,w)
udry = usat
Dry Rock Shear Modulus Does Not Change

## Slide 29: Scenario Modeling – Fluid Substitution
Original Reservoir Conditions
Oil Over Water
4570 5740
5750
5020
100m Oil Production
Oil Replaced by Water
4570 5240 5740
5750
5020
-0.11 0.00
0.05 -0.67
0.11
-0.11
-0.02
0.68
.046
 | Velocity | Density | Imped
Overburden | 2500 | 2.30 | 5750
Oil Sand | 2250 | 2.03 | 4570
Swept Sand* | 2454 | 2.14 | 5240
Water Sand | 2673 | 2.15 | 5740
Underburden | 2250 | 2.23 | 5020
 | * Swept sand has 10% residual oil |  | 

## Slide 30: Scenario Modeling – Fluid Substitution

## Slide 31: References
Pant, D. R., & Greenhalgh, S. A. (1989). Lateral Resolution in Seismic Reflection-A Physical Model Study. Geophysical Journal International, 97(2), 187–198. https://doi.org/10.1111/j.1365-246X.1989.tb00495.x
Russell, B. (2015). AVO and Inversion -Part 1 Introduction and Rock Physics. http://muhendislik.istanbul.edu.tr/jeofizik/wp-content/uploads/2015/04/Dr.-Brain-Russell-Lecture-Part-1.pdf

## Slide 32: Fluid Substitution Using Gassmann’s Equations